Deleting Chain Algorithm

# Text boxes

P 0                                                                    │

│  K7      START     A0       B0       C0       K2                K1   │

├──] [──────] [──────] [──────] [──────] [──┬───]/[───────────────( )──┤

│                                           │                          │

│  K1                                       │                          │

├──] [──────────────────────────────────────┘                          │

│                                                                      │

│                                                                      │

│  K1       A1       K3                                           K2   │

├──] [──────] [──┬───]/[──────────────────────────────────────────( )──┤

│                │                                                     │

│  K2            │                                                     │

├──] [───────────┘                                                     │

│                                                                      │

│  K2       B1       K4                                           K3   │

├──] [──────] [──┬───]/[──────────────────────────────────────────( )──┤

│                │                                                     │

│  K3            │                                                     │

├──] [───────────┘                                                     │

│                                                                      │

│  K3       C1       K5                                           K4   │

├──] [──────] [──┬───]/[──────────────────────────────────────────( )──┤

│                │                                                     │

│  K4            │                                                     │

├──] [───────────┘                                                     │

│                                                                      │

│  K4       C0       K6                                           K5   │

├──] [──────] [──┬───]/[──────────────────────────────────────────( )──┤

│                │                                                     │

│  K5            │                                                     │

├──] [───────────┘                                                     │

│  K5       B0       K7                                           K6   │

├──] [──────] [──┬───]/[──────────────────────────────────────────( )──┤

│                │                                                     │

│  K6            │                                                     │

├──] [───────────┘                                                     │

│                                                                      │

│                                                                      │

│  K6       C0       K1                                           K7   │

├──] [──────] [──┬───]/[──────────────────────────────────────────( )──┤

│                │                                                     │

│  K7            │                                                     │

├──] [───────────┘                                                     │

│                                                                      │

│  K1                                                             YA   │

├──] [────────────────────────────────────────────────────────────(S)──┤

│  K2                                                             YB   │

├──] [────────────────────────────────────────────────────────────(S)──┤

│  K3                                                             YC   │

├──] [────────────────────────────────────────────────────────────(S)──┤

│  K4                                                             YC   │

├──] [────────────────────────────────────────────────────────────(R)──┤

│  K5                                                             YB   │

├──] [────────────────────────────────────────────────────────────(R)──┤

│  K6                                                             YA   │

├──] [────────────────────────────────────────────────────────────(R)──┤

│                                                                      │

#program mazak

#def	START	x0.0	;Button "Start"

#def	A0	x1.0	;Motor A in

#def	A1	x1.1	;Motor A out

#def	B0	x1.2	;Motor B in

#def	B1	x1.3 	;Motor B out

#def	C0	x1.4 	;Motor C in

#def	C1	x1.5 	;Motor C out

#def	YA	y0.1	;Motor A go out  (command)

#def	YB	y0.2	;Motor B go out  (command)

#def	YC	y0.3	;Motor C go out  (command)

#reg 	bit 	K1,K2,K3,K4,K5,K6,K7	;Internal users registry of the step

ld	K7

and	START

and	A0

and	B0

and	C0

or	K1

anc	K2

wr	K1

ld	K1

and	A1

or	K2

anc	K3

wr	K2

ld	K2

and	B1

or	K3

anc	K4

wr	K3

ld	K3

and	C1

or	K4

anc	K5

wr	K4

ld	K4

and	C0

or	K5

anc	K6

wr	K5

ld	K5

and	B0

or	K6

anc	K7

wr	K6

ld	K6

and	C0

or	K7

anc	K1

wr	K7

ld	K1

set	YA

ld	K2

set	YB

ld	K3

set	YC

ld	K4

res	YC

ld	K5

res	YB

ld	K6

res	YA

Possible problems of this algorithm:

System may remain in the given step so short time that the solenoid can’t shift the valve to the new position.

The program is inactive after the start, because step seven (end state) variable K7 is false. You can add parallel line to K7 switch at line one which is true only in first PLC cycle over PLC start.